## Slide 1: SEPIC Converter as A Constant Current LED Controller
Nick Cardamone – Electronics 3 – Nov 18 2022

## Slide 2: Background
Did coop terms working at LED lighting company designing LED controllers
Use scrap light engine for a desk lamp
Currently use a bench supply to power the light engine

## Slide 3: Hardware Goals
I have a need for a contant current power supply (not a channel of a bench supply) to use to power my desk lamp
Pot
12V Wall Wart
Previous Prototype
No Bluetooth

## Slide 4: Presentation Overview
Background and Motivation
Problem Statement and Hardware Goals
Circuit Diagram
PCB Layout
PCB 3D View
Simulations
Design Methodology
Left TODO

## Slide 5: Circuit Diagram
Sepic converter with current feedback

## Slide 6: Prototype
Open Loop Only

## Slide 7: PCB Layout
Layer Stack: Top, Gnd Plane, Gnd Plane, Bottom

## Slide 8: PCB

## Slide 9: Simulations
Still large LED current ripple (called flicker in industry)
Undesirable but not end of the world

## Slide 10: Thermals
Max Temp: 56.6C (Input inductor on prototype)

## Slide 11: Design Steps
Search through Digikey for SEPIC Converter IC
Read datasheet
Power Stage: convert design equations into code, brute force for component values
Compensator
  Bode plot of power stage transfer function
  Bode plot of 1/feedback transfer function
  Intersection needs closure of 20 dB/dec for 45 degrees of phase margin
  RHPZ is a problem, put converter into DCM to eliminate problem
Simulate circuit (LTSPICE) and iterate and refine component values

## Slide 12: Left todo
PCBs arrive today/ there are on a truck now (ordered a week late because I had covid)
Components need to be soldered on
Component values need to be finalized
Encasement needs to be made (probably out of Al, PCB submerged in oil for passive cooling)
Simulate PCB with Ansys sim tool (sim tool doesn’t have good documentation that I can find)
Characterize converter and generate plots for final report

## Slide 13: Design Module 1 PCBs
(why I was a week late ordering)